## Slide 1: Computer Networking New Technical College Campus

## Slide 2: About Modern Technical College Campus
The new branch of the technical college is designed as a modern, technology-driven campus that supports academic learning, administration, and advanced computing needs. The campus consists of four main buildings.
This technical college branch is a fully integrated academic environment that combines:
Administrative efficiency
Practical engineering education
Advanced computing and research
Rich learning resources

## Slide 3: Network Design Goals
High availability and reliability
Secure communication between buildings
High-speed access for labs
Easy management and monitoring
Scalability for future growth
GOALS

## Slide 4: Modern Technical College Campus buildings
Administration
administrative offices, handling student records, finance, human resources, and overall campus operations.
01
Engineering
Provides classrooms, workshops, and laboratories for hands-on training and practical education in various engineering disciplines.
02
Computer Science
Serves as the technology hub with advanced computer labs and facilities for programming, software development, AI, and cybersecurity studies.
03
Library
Acts as a learning and research center offering books, digital resources, study spaces, and access to academic databases.
04

## Slide 5: Administration Building
Student registration and records
Finance and payroll
Human resources
Academic coordination
IT and network control offices
Purpose
This building serves as the operational and management center of the college.
Secure wired LAN for staff
Limited guest Wi-Fi for students
Strong access control and data protection
Technical Requirements
Key Functions
Office computers for staff
Secure access to student information systems
Internal servers (or access to centralized data center)
High availability and secure networking
Printers, scanners, and document management systems
Networking Needs

## Slide 6: Engineering Building
Electrical Engineering
Mechanical Engineering
Civil Engineering
Electronics and Communication
Purpose
This building supports hands-on engineering education and applied technical training.
High-power electrical supply for equipment
Wired network connections for lab machines
Lab management software
Safety and access control systems
Facilities
Departments Typically Included
Lecture halls
Engineering laboratories
Workshops (e.g., circuits, robotics, materials)
Faculty offices
Technical Requirements

## Slide 7: Computer Science Building
Computer Science
Software Engineering
Artificial Intelligence
Data Science
Cybersecurity
Purpose
This is the core technology hub of the campus.
Very high bandwidth
Wired Ethernet for labs
Secure segmentation (VLANs)
Controlled internet access for experiments
Specialized Computer Labs
Departments and Programs
High-performance PCs or workstations
Virtualization and cloud platforms
Isolated lab networks for cybersecurity training
Central servers for code repositories and databases
Networking Needs

## Slide 8: Library Building
Reading areas
Group study rooms
Digital library stations
Quiet zones
Printing and scanning services
Purpose
The library acts as a knowledge and research center.
Online academic databases
E-books and journals
Learning management system access
Research software tools
Technical Requirements
Facilities
Public computers for students
Strong Wi-Fi coverage
Content filtering and access control
Quiet and low-noise infrastructure
Digital Services

## Slide 9: Campus Buildings & Users
Computer Science Building
3 Labs × 25 PCs = 75 PCs
Engineering Building
3 Labs × 25 PCs = 75 PCs
Library Building
3 Labs × 25 PCs = 75 PCs
25%
Total PCs FOR 3 studding buildings = 225
25%
25%

## Slide 10: Network Topology design
Library
Administration
Computer Science
Engineering

## Slide 11: Users / Devices per Building
Category | PCS | Wireless APs
Administration Building | 75 | 6
Engineering Building | 75 | 4
Computer Science Building | 75 | 6
Library | 75 | 4
PCS NUMBER
300

## Slide 12: Building LAN Subnets
VLAN subnet |  | Assets | Usable Range
10 | 10.10.10.0/24 | 255.255.255.0 | 10.10.10.1 – 10.10.10.254
20 | 10.10.20.0/24 | 255.255.255.0 | 10.10.20.1 – 10.10.20.254
30 | 10.10.30.0/24 | 255.255.255.0 | 10.10.30.1 – 10.10.30.254
40 | 10.10.40.0/24 | 255.255.255.0 | 10.10.40.1 – 10.10.40.254
50 | 10.10.50.0/24 | 255.255.255.0 | 10.10.50.1 – 10.10.50.254
60 | 10.10.60.0/24 | 255.255.255.0 | 10.10.60.1 – 10.10.60.254

## Slide 13: Main Topology
Star topology is used within each building.
Centralized control improves performance and management.
All buildings connect to a central core network.
Fiber optic cables connect buildings.
Network Topology

## Slide 14: High-Level Topology
Core (Administration Data Room): ​
  2× Layer-3 Core Switches (redundant)​
  Firewall at the edge + ISP Router​
  Wireless Controller + Servers
Distribution/Access (each building):​
  Access switches (PoE) for PCs + APs

## Slide 15: High-Level Topology
Inter-building links:
Fiber trunk links from Admin (core) to each building (star topology)​
Packet Tracer diagram should show​
ISP ↔ Router ↔ Firewall ↔ Core L3 Switches​
Core ↔ (fiber trunks) ↔ building access switches​ VLANs on each building switch, trunk uplinks, APs mapped to SSIDs/VLANs

## Slide 16: Internet Access
Priority given to academic and lab traffic.
Bandwidth management for fair usage.
Guest access is limited.
What are we working on

## Slide 17
Different IP ranges for each building.
Improves security and network management.
VLANs separate traffic between departments.
Reduces broadcast traffic.
IP Addressing & VLANs

## Slide 18
VLAN | NAME | WHO
10 | ADMIN-STAFF | admin offices PCs
20 | ADMIN-SERVERS | servers/data center
30 | ENG-FACULTY | engineering staff
40 | ENG-LABS | engineering lab PCs
50 | CS-FACULTY | CS staff
60 | CS-LABS | CS lab PCs
70 | LIB-STAFF | library employees
80 | LIB-PUBLIC | library public PCs
90 | STUDENT-WIFI | authenticated students
100 | GUEST-WIFI | internet only
200 | MGMT | device management

## Slide 19: Building LAN Subnets

## Slide 20: Infrastructure & Point-to-Point Links (/30)

## Slide 21: Server Network Subnet

## Slide 22: Network Devices Used
01
Routers
for internet connectivity.
switches
JCore and access switches for internal networking.
02
Wireless access points
Wireless access points for Wi-Fi coverage.
03
Firewalls
Firewalls for security.
04
Servers
Servers for data and applications.
05

## Slide 23: Cost Calculation with Device Models (EGP)
Category | Device Type | Model (Real-World Example) | Quantity | Total Cost (EGP)
Network Devices | Core Layer-3 Switch | Cisco Catalyst 3560-24PS | 1 | 
 | Access Switches | Cisco Catalyst 2960-24TT-L | 4 | 
 | Building Routers | Cisco ISR 4331 | 4 | 
 | Main Router (R_main) | Cisco ISR 4331 | 1 | 
 | ISP Router | Cisco 2911 ISR | 1 | 
 | Firewall | Cisco ASA 5506-X | 1 | 
 | Wireless Access Points | Cisco Aironet 1832i | 4 | 
 | Servers | Dell PowerEdge R350 | 2 | 1,108,200
PCs (300) | Desktop PCs | HP 200 G4 All-in-One | 300 | 6,600,000
Cabling | Ethernet Cable | CAT6 (305m box) | 3 | 
 | Patch Cords & RJ-45 | Standard CAT6 accessories | — | 26,200
TOTAL PROJECT COST |  |  |  | 7,734,400 EGP

## Slide 24: IP routing
Routing implementation is complete and verified.

## Slide 25: DHCP
Routing implementation is complete and verified.

## Slide 26: ACL
The implementation of the ACL was successful, achieving the goal of restricting access for the Engineering department while maintaining connectivity for the Administration department.

## Slide 27: Campus Login

## Slide 28: Faculty selection

## Slide 29: Computer science Program

## Slide 30: Engineering Departments

## Slide 31: Library Services
The website demonstrates how the network supports real services used in a university, such as portals and information systems, and validates DNS and server functionality.

## Slide 32: Conclusion
Strong separation using VLANs + ACLs (Admin protected, Guest isolated)
Easy scalability (/24 per department, OSPF routing-ready)
Centralized services in Admin (servers + controller) with fiber backbone to buildings

## Slide 33: Team members
Adel sobhy 23101780
Yassin Ali Attia 23101505
Youssef Moharm 23101517
Mostafa Waleed 23101602
Abdelrahman hamed 23101420
Veronica Kamil 23100810
Kerolos nader 23101441
Ali hassan 23101422

## Slide 34: ANY QUESTIONS ?
THANK YOU
super visor doc / Essam Abdellatif